## Slide 1: Conway’s Game of Life on FPGA

## Slide 2: What is Conway’s Game of Life?
Notes: It’s a cellular automaton invented by John Conway in 1970
Cellular automaton is a discrete model studied in several sciences
Consists of a regular grid of cells
Each cell has a finite number of states (like dead/alive)

## Slide 3
Notes: - Conway game of life uses the so called moore neighborhood

## Slide 4: Underpopulation
Any live cell with fewer than two live neighbors dies

## Slide 5: Overcrowding
Any live cell with more than three live neighbors dies

## Slide 6: Survival
Any live cell with two or three live neighbors lives on

## Slide 7: Birth
Any dead cell with three live neighbors will be born

## Slide 8
Object examples:
Stable:
Oscillating:
Glider:
Special cases (f-Pentomino):
Notes: Blinker: 2 cycles
Bipole: 2 cycles
Oktagon: 5 cycles
f-Pentomino: chaotic structure, more than 1000 generations chaotic -> results in oscillating state

## Slide 9
Live Demo
Notes: Pulsator: 15 cycles

## Slide 11: Process

## Slide 13: Implementation
Notes: System runs at 106.6 Mhz
Output Resoulution is fixed to 1280*1024
For Readability and to safe memory I decided to calculate a lattice of 80 * 64 cells

## Slide 15: Design stupidity?
How the automaton could be even faster than it is right now?

## Slide 16
Current
Possible
Notes: Currently the process is build up like a loop over all cells:
- Easy to develop and fits requirements
<-> not the fastest possible solution: Divide Grid in subgrids and run the loop on them
Needed changes: arbiter needed that controls the ram access and so.

## Slide 17
Combinational Circuit
Memory
Notes: Calculate the state in an combinational circuit and write result for each cell back to memory

## Slide 18: Possible Extensions

## Slide 19
Reset Function
Easy Initializer
Direct Deploy
Iteration Counter

## Slide 20: Thank you!
Feel free to checkout the project on GitHub:
https://github.com/johannes5117/ConwayVHDL-Spartan6

## Slide 21: Images:
Images on slide 8 are from Wikipedia:
  https://de.wikipedia.org/wiki/Conways_Spiel_des_Lebens
The other images were self-painted